| Text Page# | Section(s) | 2008 Update Summary | TRC | GLPC | LCBOC |
| --- | --- | --- | --- | --- | --- |
|  | 1.07.01 & 2.01.01 | 2008 ULDC Map Update – Accurately Reflect Airport Overlay Depiction, Accurately Reflect 400’ Corridor Overlay Depth, Rezone Public Schools to OI, Rezone Public Parks to CON, & Rezone Public Greenspaces to CON | Approval | Approval | Approval |
| 3 | 1.07.04, 1.08.02, 1.09.01 | Update Table of Contents, List of Applicable Codes, Code Reference Guide, and Acronyms | Approval | Approval | Approval |
| 4 | 1.09.02 | Change lot of record definition to reflect subdivision regulations adoption on September 6th 1972 | Approval | Approval | Approval |
| 4 | 1.09.02 | Investigate adding lot by default definition for lots created by road design | Approval | Approval | Approval |
| 5 | 2.03.03 | Allow Light Industry in Heavy Manufacturing (M-2) | Approval | Approval | Approval |
| 5 | 2.03.03 | Remove multifamily from use chart for MAZ | Approval | Approval | Approval |
| 6 | 2.03.03, 4.03.18, & 4.03.19 | Investigate and update Landfill regulations to reflect allowance in MAZ III | Approval | Approval | Approval |
| 6 | 4.01.01(F) | Investigate Lot Width Conflict with Health Department Regulations | Approval | Approval | Approval |
| 7 | 4.04.02 (D) & 6.01.02(F)(2)(a) | Fix 25 lot discrepancy on Cul-de-sac design standards | Approval | Approval | Approval |
| 7 | 4.04.03(E) | Investigate Eliminating Additional Rear Setback in Double Frontage Lot Standards | Approval | Approval | Approval |
| 7 | 4.04.02(H), 4.04.03(G), 6.01.02, 6.03.01(A), 6.03.02 (B), 6.03.05, | Investigate requiring a 10’ utility easement on each side of every street and clarify when the applicant is responsible for utilities | Approval | Approval | Approval |
| 8 | 4.04.04 (B)(1) | Remove local water/sewer connection requirements for Family Ties. | Approval | Approval | Approval |
| 9 | 4.04.04(C)(3)(b) | Require tracts to obtain and/or share 60' of frontage on a public road | Approval | Approval | Approval |
| 9 | 4.06.00(D)(2) | Remove multi-family density requirement | Approval | Approval | Approval |
| 9 | 4.07.04 (A)(2) | Investigate Reducing Shrub Height at Installation | Denial | Denial | Denial with conditions |
| 9 | 4.07.06 | Investigate adding multi-family to buffering requirements | Approval | Approval | Approval |
| 9 | 5.03.03(A) | Investigate Allowing Mobile Food Services in MAZ II and MAZ III | Approval | Approval | Approval |
| 10 | 6.01.02(E)(i) | Require 30’ setback for gated properties | Approval | Approval | Approval |
| 10 | 6.01.03(D)(9) | Investigate 2 ft overhang for parking spaces that do not abut a sidewalk or a landscaped area | Denial | Denial With Conditions | Denial |
| 10 | 6.03.04(F) | Prohibit Injection Wells | Approval | Approval | Approval |
| 10 | 9.03.00 | Reduce authority within the administrative waiver process | Approval | Approval | Approval |
| 10 | 10.01.02 | Change timing and standards for completeness reports | Approval | Approval | Approval |
| 11 | 10.02.01( C) | Ensure support data can be required if necessary | Approval | Approval | Approval |
| 11 | 10.02.02(A) & 10.02.04 | Require preliminary plat approval before improvement plan approval | Approval | Approval | Approval |
| 11 | 10.02.05(A)(5) & 10.03.00 | Change Notice Requirements and have as a courtesy the County to attempt to notify property owners within ¼ mile or 1320 ft of a proposed zoning decision or decision that affects a specific parcel of land. | Approval | Approval With Conditions | Approval With Conditions |
| 12 | 10.06.00 & 10.06.01(A) | Add land disturbance language for secondary permittees | Approval | Approval | Approval |
| 13 | Fee Schedule & 10.02.04 | Discourage submittal of incomplete plans by requiring an improvement plan checklist, resubmittal fees, and an update to reflect changes in notification. | Approval | Approval | Approval |
| 14 | Application | Change GLPC and ZBOA Case Deadlines and Include Notice Courtesy Language | Approval | Approval | Approval |
|  |  | Shade ULDC Tables |  |  |  |

| 1.07.04, 1.08.02, 1.09.01 | Update Table of Contents, List of Applicable Codes, Code Reference Guide, and Acronyms |
| --- | --- |

1.07.04 Building and Construction Codes Each building and construction code listed in Section 1.07.04 (A) through (M) is hereby adopted by reference as if set forth in its entirety. The following standard building codes as approved by the State of Georgia include any attachments, future editions, and amendments.

A.  2006 International Building Code SBCCI Standard Building Code (International Building Code) with Georgia Amendments and including Appendix A;

B.  2006 International Fuel Gas Code SBCCI Standard Gas Code (International Fuel Gas Code) with Georgia Amendments;

C. 2006 International Mechanical Code SBCCI Standard Mechanical Code (International Mechanical Code) with Georgia Amendments;

D.  2006 International Plumbing Code SBCCI Standard Plumbing Code (International Plumbing Code) with Georgia Amendments;

E. 2003 International Existing Building Code with Georgia Amendments SBCCI Existing Building Code;

F. SBCCI Standard Housing Code (International Property Maintenance Code);

G. 2005 National Electric Code with Georgia Amendments;

H. National Fire Protection Code

I.  2000 International Energy Conservation Code with Georgia Amendments;

J.  2006 International Fire Code with Georgia Amendments;

K. 2006 International Residential Code CABO 1 and 2 Family Dwelling Code (International Residential Code) with Georgia Amendments and including Appendix E;

L.  1997 Georgia Accessibility Code

M.  2000 Life Safety Code

1.08.02 Responsibility for Interpretations

C.  Should the enforcement of a building or construction code listed in Section 1.07.04 create a conflict Table 1.08.02(C) shall govern the primary and supplemental enforcement of that building or construction code:

Table 1.08.02(C).  Code Reference Guide

| Area | Primary Code | Supplement Code |
| --- | --- | --- |
| Occupancy Classification | LSC | IBC |
| Building Construction Types Including allowable height, allowable building areas, and the requirements for sprinkler protection related to minimum building construction types. | IBC | LSC |
| Means of Egress | LSC | NONE |
| Standpipes | IBC | IFC |
| Interior Finish | LSC | NONE |
| HVAC Systems | IMC | NONE |
| Vertical Openings | LSC | NONE |
| Sprinkler Systems minimum construction standard | LSC | NONE |
| Fire Alarm Systems | LSC | NONE |
| Smoke Alarms and Smoke Detection Systems | State Statute and LSC | NONE |
| Portable Fire Extinguishers | IFC | NONE |
| Cooking Equipment | LSC and NFPA 96 | NONE |
| Fuel Fired Appliances | IFGC | NFPA 54 or IFGC |
| Liquid Petroleum Gas | NFPA 58 | NFPA 54 or IFGC |
| Compressed Natural Gas | NFPA 52 | NONE |

1.09.01 Acronyms

IBC – International Building Code, IMC – International Mechanical Code, LSC – Life Safety Code, IFC – International Fire Code, IFGC – International Fuel Gas Code, & NFPA – National Fire Protection Association

| 1.09.02 | Change lot of record definition to reflect subdivision regulations adoption on September 6th 1972 |
| --- | --- |

Lot of record. A lot which is part of a subdivision plat recorded in the office of the Clerk of Superior Court, or a parcel described by metes and bounds, the description of which has was been so recorded before the adoption of subdivision regulations on September 6th 1972.

| 1.09.02 | Investigate adding lot by default definition for lots created by road design |
| --- | --- |

Lot by default. A lot which was once whole but divided into parts through the acquisition of public property or construction of a public road.  Each piece of the once whole lot shall henceforth be considered a separate and independent lot.  The lots shall be governed by Section 9.01.02 Nonconforming Lots of Record.

| 2.03.03 | Allow Light Industry in Heavy Manufacturing (M-2) |
| --- | --- |
| Zoning Districts: P – Permissible S1 – Permissible Subject to Supplemental Standards Blank – Prohibited | E-A | R-A | CON | R-1 | R-21 | R-10 | OI | C-C | C-G | C-H | M-1 | M-2 | M-3 | MAZ-I | MAZ-II | MAZ-III | PD (Section 4.06.00) | IS |
| Manufacturing |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Light Industry |  |  |  |  |  |  |  |  |  | P∞ | P | P |  |  | S | P |  |  |
| Heavy Industry |  |  |  |  |  |  |  |  |  |  |  | P | P |  |  | P |  |  |

| 2.03.03 | Remove multifamily from use chart for MAZ |
| --- | --- |
| Zoning Districts: P – Permissible S1 – Permissible Subject to Supplemental Standards Blank – Prohibited | E-A | R-A | CON | R-1 | R-21 | R-10 | OI | C-C | C-G | C-H | M-1 | M-2 | M-3 | MAZ-I | MAZ-II | MAZ-III | PD (Section 4.06.00) | IS |
| Multi-Family* |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | S | ( |  |

| 2.03.03, 4.03.18, & 4.03.19 | Investigate and update Landfill regulations to reflect allowance in MAZ III |
| --- | --- |

### 4.03.18 Sanitary Landfills

Sanitary landfills, together with necessary buildings and machinery for landfill operations, are allowable in the M-3, MAZ III, and IS zoning districts, subject to the standards of the zoning district and the supplemental standards of this section.

### 4.03.19 Inert Landfills

Inert landfills, together with necessary buildings and machinery for landfill operations, are allowable in the M-3, MAZ III, and IS zoning districts, subject to the standards of the zoning district and the supplemental standards of this section.

| 4.01.01(F) | Investigate Lot Width Conflict with Health Department Regulations |
| --- | --- |

Table 4.01.01(F).  Standards for Lot Area, Width, and Impervious Surface.1

| Zoning District | Minimum Lot Area (Sq. ft.) | Minimum Lot Width (feet) | Maximum Impervious Surface Ratio (Percent |
| --- | --- | --- | --- |
|  | With Individual Well Water | With Central Water System | With Individual Well Water | With Central Water System |  |
| E-A | 217,800 | 217,800 | 210 | 200 | 15 |
| R-A | 108,900 | 108,900 | 150 | 100 | 20 |
| CON | 43,560 | 43,560 | N/A | N/A | 15 |
| R-1 | 43,560 | 43,560 | 150 120 | 150 120 | 30 |
| R-212 | 43,560 | 21,780 | 120 | 100 | 40 |
| R-103 | 43,560 | 10,000 | 120 | 80 | 50 |
| OI | 43,560 | 10,000 | 120 | 100 | 75 |
| C-C | 43,560 | 10,000 | 120 | 80 | 75 |
| C-G | 43,560 | 10,000 | 120 | 80 | 75 |
| C-H | 43,560 | 10,000 | 120 | 100 | 85 |
| M-1 | 43,560 | 30,000 | 120 | 100 | 85 |
| M-2 | 43,560 | 43,560 | 150 | 150 | 85 |
| M-3 | 43,560 | 43,560 | 150 | 150 | 85 |
| IS | As established in the environmental permit. |
| MAZ | See Section 4.02.04. |

1Installation of septic systems are subject to the approval of the Board of Heath.  See Section 6.02.00

2Development within the R-21 zoning district may be permitted with septic tanks, subject to the approval of the Board of Health.

3Development within the R-10 zoning district at the 10,000 sqft lot size shall require both a central water supply system and community sanitary sewer system.  Development shall be permitted on individual wells or on individual septic tanks, subject to the approval of the Board of Health.

| 4.04.02 (D) & 6.01.02(F)(2)(a) | Fix 25 lot discrepancy on Cul-de-sac design standards |
| --- | --- |

### 4.04.02 General Design Standards for Subdivisions

D. A subdivision shall have at least two (2) entrances if the subdivision is planned to have twenty-five (25) or more lots.

F. Design standards

2. Cul-de-sacs

a. Permanent cul-de-sacs shall be limited in length so that each cul-de-sac serves as street access for no more than twenty-four (24) twenty-five (25) lots.

| 4.04.03(E) | Investigate Eliminating Additional Rear Setback in Double Frontage Lot Standards |
| --- | --- |

E. Double frontage or through lots shall be prohibited, except where essential to provide for separation of residential development from arterial or collector streets and railroad rights-of-way.

1. Lots which abut arterial or collector streets and railroad rights-of-way on the rear lot line shall have the minimum rear yard setback as required by the zoning district, plus an additional thirty (30) feet.

2. Within this additional thirty (30) feet rear yard, a planted, non-encroachable buffer strip shall be provided, pursuant to the standards set forth in Section 4.07.06.

| 4.04.02(H), 4.04.03(G), 6.01.02, 6.03.01(A), 6.03.02 (B), 6.03.05, | Investigate requiring a 10’ utility easement on each side of every street and clarify when the applicant is responsible for utilities |
| --- | --- |

### 4.04.02 General Design Standards for Subdivisions

H. General requirements for all other utilities When the applicant constructs or upgrades infrastructure for a subdivision the applicant shall make the necessary arrangements with the appropriate utility companies for the installation of utilities to assure that all lots have adequate gas, electrical, cable, and telephone communication services.

### 4.04.03 Design Standards for Blocks, Easements, and Lots

G. Easements

1. All lots within a subdivision shall provide easements for stormwater drainage, water systems, sanitary sewer systems, gas lines, electric lines, cables, telephone lines, and utility poles. Standards for such utility easements are set forth in Section 6.03.02.

### 6.01.02 Streets and Rights-of-Way

11. Medians

b. Median in a street with curb and gutter

i. Additional right-of-way will be required to provide a shoulder of at least ten (10) feet width measured from back of curb to right-of-way.

ii. Utility easements will be required beyond the right-of-way for the installation of utilities. The width of such easements will be as required by the County Engineer after review of the Preliminary Plat and preliminary construction plans of the subject subdivision.

6.03.00 REQUIREMENTS REGARDING POTABLE WATER, SANITARY SEWER, AND OTHER UTILITIES

### 6.03.01 Generally

A. All development shall include adequate provision for utility infrastructure in full compliance with the standards of Section 6.03.00.

### 6.03.02 Requirements for All Utilities

B. The location, design, and construction of utilities shall comply with the Lowndes County Technical Standards Manual.

F.  A minimum 10’ utility easement is required outside of the right-of-way for the provision of utilities.

### 6.03.05 Other Utility Requirements

A. When water, sewer, electrical power, telephone, or cable television facilities are installed and intended to be owned, operated, or maintained by a public utility or any entity other than the property owner or developer, the ownership of such utility or facility shall be transferred to the service provider.

B. All lines for electricity, telephone, cable television, streetlights, and gas distribution (exclusive of transformers or enclosures containing electrical equipment, including, but not limited to, switches, meters, or capacitors) shall be placed underground within easements or dedicated public rights-of-way.

| 4.04.04 (B)(1) | Remove local water/sewer connection requirements for Family Ties. |
| --- | --- |

### 4.04.04 Specific Provisions for Family Ties Land Division

Applicability The provisions of this section apply to land divisions in the E-A or R-A zoning district.

B. Exemptions from platting requirements

1. Lots created as a result of the Family Ties Land Division are exempt from the subdivision standards set forth in Section 4.04.00, the water/sewer connection requirements in Chapter 6, and the platting requirements set forth in Chapter 10, provided that the lots are conveyed to a grandparent, parent, stepparent, adopted parent, sibling, child, stepchild, adopted child, or grandchild of the owner of the parcel to be divided (parent parcel).  These exemptions do not exclude any state requirements for development.

| 4.04.04(C)(3)(b) | Require tracts to obtain and/or share 60' of frontage on a public road |
| --- | --- |

b. Share one (1) access driveway that provides access to all lots.

i. The access driveway shall be sixty (60) feet wide, shall begin at a public road, and shall be recorded as an easement with access rights to all lots.

ii. The access driveway shall be an all weather road with a minimum clearance of twenty (20) feet in width and twelve (12) feet in height.

| 4.06.00(D)(2) | Remove multi-family density requirement |
| --- | --- |

2. For multi-family development with a PD District, the density shall not exceed twelve (12) units per acre; and

| 4.07.04 (A)(2) | Investigate Reducing Shrub Height at Installation |
| --- | --- |

2. Shrubs shall be at least eighteen (18) inches in height at the time of installation.

| 4.07.06 | Investigate buffering requirements |
| --- | --- |

C. Buffer Area Standards Table 4.07.06(C). Buffer Area Standards.

| Proposed Land Use | Adjacent Zoning District | Minimum Buffer Area* |
| --- | --- | --- |
| Industrial | E-A, R-A, CON, R-1, R-21, R-10 | 40 feet* |
| Multi Family, Commercial or Mixed-use areas | E-A, R-A, CON, R-1, R-21, R-10 | 30 feet* |
| Office or Institutional | E-A, R-A, CON, R-1, R-21, R-10 | 20 feet* |

| 5.03.03(A) | Investigate Allowing Mobile Food Services in MAZ II and MAZ III |
| --- | --- |

### 5.03.03 Mobile Food Services

A. Applicability

Mobile food services are permissible on vacant lots or on lots containing a business in the OI, C-C, C-G, C-H, MAZ II, MAZ III, M-1, and M-2 zoning districts in accordance with the standards of this section.

| 6.01.02(E)(i) | Require 30’ setback for gated properties |
| --- | --- |

E. Private roads

i. Development with private streets or drives may erect a security gate at the entrance provided that the security gate is equipped with a pass key system or an emergency alarm activated gate to provide access for emergency vehicles and is located at least 30’ back from the point where the private street or drive meets the surface of the public road.

| 6.01.03(D)9 | Investigate 2 ft overhang for parking spaces for parking spaces that do not abut a sidewalk or a landscaped area |
| --- | --- |

9. Individual spaces and internal aisles shall be designed according to the standards below;

a. Parking space dimensions shall be a minimum of nine (9) feet by twenty (20) feet.

| 6.03.04(F) | Prohibit Injection Wells |
| --- | --- |

### 6.03.04 Sanitary Sewer System Requirements

F. Waste disposal through use of injection wells is prohibited.

| 9.03.00 | Reduce authority within the administrative waiver process |
| --- | --- |

A. A reduction in the minimum front, side, or rear yard setbacks for a single lot, provided one of the following standards is met:

1. The reduction is necessary in order to implement landscaping, buffer, and tree protection standards of this ULDC; or

2. The reduction is limited to a maximum of twenty (20) percent of the minimum standard for no more than two (2) setbacks.

| 10.01.02 | Change timing and standards for completeness reports |
| --- | --- |

### 10.01.02 Determination of Completeness

A. All applications shall be complete before acceptance for review and decision-making. A determination of completeness is a determination that all required documents and plans have been submitted in sufficient number, and that all fees have been paid. A determination of completeness is not a determination of compliance with substantive standards and criteria.

B. The County Manager shall determine, within five (5) days of receipt of an application, whether the application is complete.

C. If the County Manager determines that the application is not complete, the County Manager shall send notice to the applicant identifying the deficiencies. The applicant shall have thirty (30) five (5) days from the date of notice to correct the deficiencies. Until the applicant corrects the deficiencies, no further action shall be taken for processing the application. If the applicant fails to correct the deficiencies within the thirty (30) five (5) day period, the application shall be deemed withdrawn, and the fees, application, and materials submitted shall be returned.

D. If the County Manager determines that the application is complete, the application shall be processed for review and action in accordance with the procedural requirements set forth in this chapter.

| 10.02.01( C) | Ensure support data can be required if necessary |
| --- | --- |

C. Required support data and plans Specified plat, plan, and site plans submitted with applications for subdivision plat approval and development plan approval may shall be required to be accompanied by the required supporting data and plans as described below.

| 10.02.02(A) & 10.02.04 | Require preliminary plat approval before improvement plan approval |
| --- | --- |

- The purpose of the preliminary plat is to safeguard the applicant from unnecessary loss of time and expense in preparation of a subdivision plat which does not conform with the specifications of the subdivision regulations set forth in this ULDC. The preliminary plat requires only approximate accuracy of scale and dimension. Public agencies having jurisdiction will review preliminary plats regarding matters within their jurisdiction. The preliminary plat is required to be approved before improvement plans are submitted.  In addition to the application requirements set forth in Section 10.02.01, the following information shall be required for a preliminary plat:

### 10.02.04 Submittal Requirements for Improvements Plans

Plans for infrastructure, utilities, and other improvements shall be submitted after an approved preliminary plat has been obtained demonstrating compliance with the improvement plan checklist, the requirements of Chapter 6, the Technical Standards Manual, and other engineering and construction standards of Lowndes County.

| 10.02.05(A)(5) & 10.03.00 | Change Notice Requirements and have as a courtesy the County to attempt to notify property owners within ¼ mile or 1320 ft of a proposed zoning decision or decision that affects a specific parcel of land. |
| --- | --- |

### 10.02.05 Submittal Requirements for Rezoning Applications

A. In addition to the application materials specified in Section 10.02.01, applications for amendment of the Lowndes County Zoning Map shall include the following:

5. A list of all current owners of record for properties located immediately adjacent to or directly across a public street or railroad right-of-way from the subject property. The list shall include the current names, mailing addresses, and tax Map-Parcel numbers as reflected on the current tax roll of Lowndes County.

10.03.00 NOTICE REQUIREMENTS

### 10.03.01 Zoning Decisions

A. At least fifteen (15) but not more than forty-five (45) days prior to the date of hearing, notice shall be published within a newspaper of general circulation in the County stating the date, time, place, and purpose of the hearing.

B. If the zoning decision is for the rezoning of property and the rezoning is initiated by a party other than the County, then:

1. The published notice shall also include the location of the property, the present zoning classification of the property, and the proposed zoning classification of the property; and

2. A sign shall be placed in a conspicuous location on the property not less than fifteen (15) days prior to the hearing containing the nature of the request and the date, time, and place of the hearing.

3. The applicant shall provide a list of all current owners of record for properties located within ¼ mile or 1320ft of the subject property. The list shall include the current names, mailing addresses, and tax Map-Parcel numbers as reflected on the current tax roll of Lowndes County.  Property owners that are adjacent to the subject property, to include those across all right-of-way, shall be notified by certified mail.

### 10.03.02 All Other Decisions

A. At least fifteen (15) but not more than forty-five (45) days prior to the date of hearing, notice shall be published within a newspaper of general circulation in the County stating the date, time, place, and purpose of the hearing.

B. If the hearing involves only one a specific parcel or parcels of property, then:

1. The published notice shall state the location of the property; and

2. A sign shall be placed in a conspicuous location on the property not less than fifteen (15) days prior to the hearing containing the nature of the request and the date, time, and place of the hearing.

3. The applicant shall provide a list of all current owners of record for properties located within ¼ mile or 1320ft of the subject property. The list shall include the current names, mailing addresses, and tax Map-Parcel numbers as reflected on the current tax roll of Lowndes County. Property owners that are adjacent to the subject property, to include those across all right-of-way, shall be notified by certified mail.

Please Also See Fee Schedule and Application Chart on Page 13 and 14.

| 10.06.00 & 10.06.01(A) | Add land disturbance sentence |
| --- | --- |

10.06.00 ENFORCEMENT AND PENALTIES

### 10.06.01 Inspections and Enforcement Pertaining to Land Disturbing Activities

A. The Lowndes County Engineering Department will periodically inspect the sites of land-disturbing activities for which permits have been issued to determine if the activities are being conducted in accordance with the plan and if the measures required in the plan are effective in controlling erosion and sedimentation. Also, the Local Issuing Authority shall regulate both primary and secondary permittees as such terms are defined in the state general permit. Primary permittees shall be responsible for installation and maintenance of best management practices where the secondary permittee is conducting land-disturbing activities. Secondary permittees shall be responsible for installation and maintenance of best management practices where the secondary permittee is conducting land-disturbing activities.  If, through inspection, it is deemed that a person engaged in land-disturbing activities as defined herein has failed to comply with the approved plan, with permit conditions, or with the provisions of this ULDC,- a written notice to comply shall be served upon that person. The notice shall set forth the measures necessary to achieve compliance and shall state the time within which such measures must be completed. If the person engaged in the land-disturbing activity fails to comply within the time specified, he shall be deemed in violation of this ULDC.

| Fee Schedule & 10.02.04 | Discourage submittal of incomplete plans by requiring an improvement plan checklist, resubmittal fees, and an update to reflect changes in notification. |
| --- | --- |

| Application | Filing Fee | Notice Fee |
| --- | --- | --- |
| Pre-Application Conference | $0 | $0 |
| Variance | $200 | $2 for Each Adjacent Property Within ¼ mile or 1320 ft Owner and $250 for Advertisement. |
| Administrative Waiver | $0 | $0 |
| Vested Rights | $0 | $2 for Each Adjacent Property Within ¼ mile or 1320 ft Owner and $250 for Advertisement. |
| Exempt Subdivision | $50 | $0 |
| Minor Subdivision | $150 | $0 |
| Conventional Subdivision Preliminary | $400 | $0 |
| Conventional Subdivision Final | $200 | $0 |
| Development Plan | $200 | $0 |
| Improvement Plan (1st Submittal) | $300 | $0 |
| Improvement Plan (3rd Submittal and Beyond) | $350 | $0 |
| Rezoning | $350 | $2 for Each Adjacent Property Within ¼ mile or 1320 ft Owner and $250 for Advertisement. |
| Amendment | $250 | $2 for Each Adjacent Property Within ¼ mile or 1320 ft Owner and $250 for Advertisement. |
| ULDC Amendment | $200 | $2 for Each Adjacent Property Within ¼ mile or 1320 ft Owner and $250 for Advertisement. |
| Administrative Appeal | $200 | $2 for Each Adjacent Property Within ¼ mile or 1320 ft Owner and $250 for Advertisement. |
| Tower/Antenna | $250 | $2 for Each Adjacent Property Within ¼ mile or 1320 ft Owner and $250 for Advertisement. |

### 10.02.04 Submittal Requirements for Improvements Plans

Plans for infrastructure, utilities, and other improvements shall be submitted after an approved preliminary plat has been obtained demonstrating compliance with the improvement plan checklist, the requirements of Chapter 6, the Technical Standards Manual, and other engineering and construction standards of Lowndes County.

| Application | Change GLPC and ZBOA Case Deadlines and Include Notice Courtesy Language |
| --- | --- |

| Application Types | Application Requirements Section | Estimated Cost to the County | Citizen Filing Fee | Estimated Time to Process Application | Processing Deadlines |
| --- | --- | --- | --- | --- | --- |
| Exempt Subdivision | 10.02.01 & 10.01.04(G) | $93 | $50 | 3 to 10 Days | Monday for Tuesday TRC Agenda1 |
| Pre-Application Conference Request | 10.02.01 & 10.01.01 | $104 | $0 | 1 to 5 Days | Friday for Tuesday TRC Agenda1 |
| Minor Subdivision | 10.02.01 & 10.01.04(E) | $170 | $150 | 15 to 30 Days |  |
| Conventional Subdivision Preliminary | 10.02.01, 10.01.06, & 10.02.02(A) | $451 | $400 | 30 to 45 Days |  |
| Conventional Subdivision Final | 10.02.01, 10.01.06, & 10.02.02(B) | $220 | $200 | 30 to 45 days |  |
| Development Plan | 10.02.01 & 10.02.03 | $227 | $200 | 15 to 30 Days |  |
| Improvement Plan (1st Submittal) | 10.02.01 & 10.02.04 | $315 | $300 | 15 to 30 Days |  |
| Rezoning | 10.02.01 & 10.02.05 | $968 | $600* | 50 to 75 Days | 25th 5th of Month for Next Month’s GLPC Agenda and Subsequent Month’s LCBOC Agenda3 |
| Amendment to Approved Application | 10.02.01 & 10.02.06 | $902 | $500* | 15 to 75 Days |  |
| ULDC Amendment | 10.02.01 & 10.02.07 | $601 | $450* | 50 to 75 Days |  |
| Tower/Antenna | 10.02.01 & 5.05.00 | $644 | $500* | 50 to 75 Days |  |
| Variance | 10.02.01 & 9.02.00 | $631 | $450* | 45 to 60 Days | 25th 5th of Month for Next Available ZBOA Agenda2 |
| Administrative Appeal | 10.02.01 & 10.04.00 | $631 | $450* | 45 to 60 Days |  |
| Administrative Waiver | 10.02.01 & 9.03.00 | $106 | $0 | 3 to 7 Days | None |
| Vested Rights | 10.02.01 & 9.04.00 | $575 | $250* | 22 to 30 Days | None |

*Citizen Filing Fees do not include a notice fee of $2 per property owner within ¼ mile or 1320ft.  An attempt shall be made by the County to notify property owners by mail within ¼ mile or 1320 ft of the proposed action to include: location of the property, the present zoning classification of the property, the proposed zoning classification of the property and the date, time, and place of the hearing.

1.	For applications that need to be on the Technical Review Committee (TRC) Agenda, those applications turned in by Friday, October 5th at 12pm would be eligible for the TRC Meeting on Tuesday, October 9th. The TRC meets every Tuesday in the Lowndes County Administration Building located at 325 West Savannah Avenue.

2.	For applications that need to be on the Zoning Board of Appeals (ZBOA) Agenda, those applications turned in by November 5th would be on the December 4th ZBOA Agenda.  The ZBOA meets the first Tuesday of each month in the Valdosta City Hall Annex located at 300 North Lee Street.

3.	For applications that need to be on the Greater Lowndes Planning Commission (GLPC) Agenda and the Lowndes County Board of Commissioners (LCBOC) Agenda, those applications turned in by November 5th would be on the November 26th GLPC Agenda and the December 11th LCBOC Agenda.  The GLPC meet the last Monday of each month and the LCBOC meet the 2nd and 4th Tuesday of each month.  The GLPC and LCBOC meet in the Lowndes County Administration Building located at 325 West Savannah Avenue.